## Slide 1: syrmDesign with staircase airgap induction
May 2, 2017
simone.ferrari@polito.it

## Slide 2: Content
syrmDesign flowchart
New parameter definition: kt
Staircase evaluation
d-axis evaluation
Minor modifications
FEA verification

## Slide 3: syrmDesign flowchart
start
staircase evaluation
geometric definitions
d-axis evaluation
q-axis evaluation
Slot area and leakage
Torque and PF evaluation
end
NOTE:
The green blocks are added in this release. The yellow blocks are modified in this release.
The order in the performance evaluation is slightly different in the script.

## Slide 4: New tooth factor definition: kt
The new factor kt is defined as the ratio (lower than 1) between the tooth width evaluated to have a tooth induction equal to the yoke induction, and the final tooth width.
A smaller tooth cause:
a reduction of the ratio between the maximum airgap induction and the yoke induction
a possible increase of the peak of the first harmonic in the airgap, respect to the maximum induction allowed at the airgap
an increasing of the slot area, that means an higher rated current

## Slide 5: Staircase evaluation
Ideally, the airgap induction is a sinewave. The effect of the stator teeth make the airgap induction a staircase, which copy the original sine (called generator in the following slides).
In the proposed analysis, the staircase is used to evaluate the shape factor to obtain the mean value and the peak of the first harmonic of the staircase, starting from the maximum airgap induction (b*Bfe).
Using a per-unit notation, where the base value is b*Bfe, the maximum instantaneous induction allowed in the airgap is equal to 1: all the points of the wave with Bpu>1 will be saturated to 1. With kt=1, the peak of the generator wave is equal to 1 and no saturation is applied (top figure of the next slide).
With kt<1, the peak of the generator wave is increased, causing a saturation in the staircase wave. This saturation leads to a first harmonic peak higher than 1 (bottom figures of next slide)

## Slide 6: Staircase evaluation

## Slide 7: d-axis evaluation: saturation factor
To improve the estimation of the correct magnetization current (d-current), the MMF drops along the iron path should be taken into account. To do this, a saturation factor (ks) is multiplied to the evaluated d-current. This factor is the ratio between the sum of MMF drop in the most loaded tooth, in the most loaded section of the yoke (one slot pitch), in the most loaded rotor flux carrier and in the airgap, over the airgap MMF drop.
In this simplified model, the induction is imposed constant for each iron region and the field intensity is obtained from the B-H curve of the material.

## Slide 8: Minor modifications
Additional minor modification are done, as:
Correction of the Lfqpu, using the “real” geometry definition, with evaluated permeance
Correction of the ribs inductance estimation
Use of the saturated staircase for the flux carrier design
Design of the rotor for all the machine in the x-b plane (and not only the selected one). So for all the machine, the rotor flux barriers and the rotor flux carriers are designed.