## Slide 1: MaxTw - update
March, 2018
Simone Ferrari (simone.ferrari@polito.it

## Slide 2: Content
  Introduction
  Updates
  Input parameters
  Outputs

## Slide 3: Introduction
MaxTw.m is a script used in the post processing.
His aim is to build the maps in the torque-speed plane, following the mimimul losses control trajectories

## Slide 4: Updates
The main updates are:
  Much more readable scripts
  Possibility to keep into account skin effect in copper loss
  Possibility to use different iron loss models, or no iron loss
  Possibility to add mechanical loss
  Motor-generator mode
  Different kind of machines supported: SyR, PM-SyR, SPM, IM (only post process)
  Input windows

## Slide 5: Inputs
  The main input is the magnetic model of the machine (fdfq_idiq_n256.mat), selected with a windows
  All the parameters are added with a dedicated GUI (shown on right). They are:
    Motor name and general informations (pole pairs, type,…)
    Electrical limits (voltage and current)
    Map definition: limits and number of points on both axes
    Temperature of the magnetic model, and of the output maps
    Loss information: stator resistance, if use iron loss model and skin effect model, and mechanical loss model, in a polynomial expression as a function of the speed in rpm
  If the iron loss model and/or the skin effect model are selected, further windows will ask to select the models

## Slide 6: Inputs – iron loss model
Four kind of iron loss model are allowed:
  Map in idiq @ constant speed (as old version)
  Single point (as old version)
  Fit for IM, function of flux linkage, q-current and frequency
  Fit for SyR machines along MTPA, function of current and frequency
It is also possible to add a custom iron loss model. Two functions are needed: loadIronLossModel.m and calcIronLoss.m (see in syreManipulateMM\mfiles)

## Slide 7: Output
The output is not changed from the older version. They are:
  The structures DatiOpt (output) and d (input)
  Control trajectories in IdIq plane
  Efficiency, loss, voltage and current surfaces
  Extra: during the elaboration, a plot shows the analyzed T-w points and highlight in green the allowed ones, and in red the not allowed ones. Not allowed means high current/voltage or small magnetic model
  The results are saved in a new folder called [‘TwMap_’ MotorName], in the same path of the magnetic model